MAC USERS NOTE: This document is formatted using the “hidden text” feature. Text that appears on your screen display as blue text in a blue box will not print. To change this setting and print hidden text, click Preferences on the Word menu, click Print, and then select the Hidden text check box.

WINDOWS USERS NOTE: This document is formatted using the “hidden text” feature. Text that appears on your screen display as blue text in a blue box will not print. To view or turn off the “hidden text” feature go to the tools menu, click options, and then click the view tab. Select or clear the formatting marks box labelled hidden text.

This section includes a manufacturer's guide specification for Snap-Tex site fabricated, stretched fabric cover, track mounted,  acoustic flat or curved ceiling  applications. Typical applications include Snap-Tex ceiling track profiles used with a variety of acoustic substrates, with colored or printed fabrics.  This section includes performance, proprietary, and descriptive type specifications; edit to avoid conflicting requirements.

# GENERAL

## SECTION INCLUDES

In this article, select the components that are intended to be part of the content of this section and will not be included in other sections.  Keep the statements brief and concise.

### PVC track mounted, acoustic ceiling assembly, stretched fabric covering, site assembled.

### [Supplementary framing to permit secure mounting of panel.]

### Substrate support.

## RELATED SECTIONS

Utilize the following Paragraph where panels will be attached to adjacent construction.

### Section [______-____________]:  Preparation of adjacent work and substrate to receive work of this Section.

## REFERENCES

List reference standards that are included within the text of this section.  Edit the following as required to parallel any reference standards statements within this section.  Acronyms are used for well known standards.  The NFPA-701 Large Scale test is the more strenuous test and is the most widely accepted standard for fabrics not attached directly to a substrate - this test normally applies for textiles not directly applied to a substrate. E84 applies to surface-burning characteristics of fabrics not attached to substrate, as well as applying to other materials of the assembly, or the whole assembly.

### ASTM C423 - Standard Test Method for Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method.

### ASTM D5034 - Standard Test Method for Testing Breaking Loads of Woven Textiles.

### ASTM E84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

### NFPA 701 - Standard Methods of Fire Tests for Flame Propagation of Textiles and Films.

## PERFORMANCE REQUIREMENTS

Restrict statements in this article to identify system performance requirements or function criteria - where final design decisions or detailing is performed by Contractor.  NRC, Diffusion patterns, and Fire ratings will depend on acoustical substrate and fabric surface, coordinate with materials selected to ensure that acoustical performance and fire retardant class are achievable.  Note that all manufacturers test data is for assemblies constructed with representative fabrics and substrates.  A test of the exact assembly, as specified must be specified if the flame retardant characteristics of the components, or an inference from like components are not sufficient for the governing authorities.

### Fire Retardant Classification:  Class A, to ASTM E84.

NRC rating for three differing panel core materials are: 0.80 to 1.05 for TrueTone, 0.85 to 1.10 for TrueTone Hi-Impact, and 0.20 to 0.50 for Tacwall products.

### Acoustic Attenuation:  NRC [0.80,] [_____,] to ASTM C423.

### Minimum Breaking Load:  [______] N ([_____] lb), to ASTM D5034.

Ameri-Span wide fabrics are available in a number of colors, weaves, and widths.  They can also be digitally printed up to 10 feet wide, by bolt length.

### Fabric:  High content stable yarns, acoustically transparent, when covering an acoustic substrate.

### Suspended Ceiling Flatness Under Load:  [1/180.] [1/240.] [1/360.]

## SUBMITTALS

Do not request submittals if drawings sufficiently describe the products of this section or if proprietary specifying techniques are used.  The review of submittals increases the possibility of unintended variations to drawings, thereby increasing the Specifier's liability.  The following submittals are intended for review and acceptability.

### Section 01300:  Submission procedures.

### Product Data:  Submit product data for panel frame, [supports,] [suspended panels,] fabric, and rigid acoustic substrate.

### Shop Drawings:  Identify panel sizes, panel configurations, track frame profiles, fabric selections by elevation, and corner details.

### Samples:  Submit [one (1) sample,] [two (2) samples], [300 x 300 mm (12 x 12 inch)] [________] size, including panel substrate and fabric.  Sample for reviewing for color, texture, fabric tautness, alignment and pattern of weave, fabric translucency, and appearance of corners.

### Installer Certificate:  Showing installation certification by panel manufacturer.

## QUALITY ASSURANCE

### Fabricators / Installers: Trained and certified by panel manufacturer.

## MOCK-UP

Use this article for assessing full sized erected assemblies for review of construction, coordination of work of several sections, testing, or observation of operation.  If a mock-up is desired, consider removing the requirement for samples under Submittals.

### Section 01400:  Requirements for mock-up.

### Provide minimum [____x____] mm ([____x____] inches) mock-up of a panel, including acoustic substrate, fabric and a panel joint, as applicable.

### Locate [where directed.] [________.]

### Mock-up may [not] remain as part of the Work.

## DELIVERY, STORAGE, AND PROTECTION

### Section 01600:  Transport, handle, store, and protect products.

### Deliver and store panels in a dry and stable environment.

### Acclimatize fabrics for minimum 24 hours, at temperature and humidity approximating that of occupancy prior to installation.

### Protect fabric surfaces from damage.

## SPECIAL WARRANTY

This article extends the contract warranty period beyond one year.

### Section 01700:  Warranties.

### Provide a ten-year manufacturer's warranty against panel core or fabric material defects.

# PRODUCTS

## MANUFACTURERS:

### Snap-Tex International.

### Substitutions: [Refer to Section 01600.] [Not permitted.] [Refer to Instructions to Bidders.]

## MATERIALS

Select one or more of the following materials or products as appropriate to ceiling configuration required.  Delete those items not required.

### Ceiling Grid:

#### Mounting Track: Rigid PVC.

#### Suspension Assembly:  [Steel] [Aluminum] [________] grid members, suspension components, [exposed T-bar] [________] grid style.

#### Grid:  One-piece frame, hinged if required for above ceiling access, interlocking jaw, biased tension.

#### Grid Style:  [Bevel tegular.] [Square tegular.] [Radius tegular.]

### Panels:

The first choice below is standard - the next three choices are options.  Almost any absorptive substrate is adaptable including, reflective and diffusive shapes.  Panel sizes can range from 48to 120 inches.

#### Individual Panel Size:  [____] mm ([____] inches).

### Acoustic Substrate:

#### Panel:  Glass fiber core, [2.7 to 3.2 kg (6 to 7 lb) density, semi-rigid acoustical glass fiber.] [Reflective substrate.] [Diffusive substrate.] [As required to achieve acoustic attenuation, diffusion, reflection, in combination, as required.]

#### Ceiling Panel  Edge Profile:  [Radiused.] [Beveled.] [Square.]

#### Panel Nominal Thickness: [____] mm ([____] inches).

#### Panel Shape:  Refer to Drawings.

### Supplementary Frame/Furring:

#### [Wood:] [Metal:]  Of sufficient thickness to achieve panel thickness, frame integrity, support requirements, and acoustic performance requirements.

It is important that the fabric be acoustically transparent such that sound is not reflected, but absorbed by the panel core.  Usually acrylic fiber or paper-backed fabrics are unsuitable.

### Fabric Covering:

#### Fabric:  [By Owner.] [Acoustically transparent fabric, fire retardant to meet [ASTM E84] [NFPA 701]] [Ameri-Span inherently flame retardant, wide fabrics.

#### Liner: [Fabric] [Perforated Dupont Tyvek] [Snap-Span] [________] type, [3 m (10 ft)] [4.2 m (14 ft)] [4.8 m (16 ft)] wide, [acoustically transparent,] [________.]

#### [Fabric Protection:  Dupont Teflon based protectant.]

### Fastener:  [Heavy duty 25 mm (1 inch) staples.] [25 mm (1 inch) screws.] [As required, compatible with substrate frame surface.]

### Accessories:

#### Trim, special frame shapes: [As detailed.] [________.]

#### Suspension:  Wire/rods from ceiling above, size and strength to support panel dead and live loads, other imposed loads, plus safety factor.

# EXECUTION

## PREPARATION

### Do not proceed until surrounding environment is clean and dry.

### Maintain temperature, and humidity at conditions approximating those of occupancy prior to, during, and after installation.

### Ensure substrate surface is smooth, flat, and taped and sealed prior to track installation.  Directly adjoining work must be complete and dry.

### Field measure areas to receive panels; establish exact layout of units.

## INSTALLATION

### [Install [suspension grid] [furring] [tracks] to achieve nominal ceiling assembly thickness of [____] mm ([____] inches.]

### Install track plumb and level, straight with fittings, flush to achieve panel configuration.

### Fasten track frame in consistent manner, minimum 25 mm (1 inch) on center.

### Install acoustic substrate material, continuous to rear base of track.

### Cut fabric from each roll, maintaining sequence of drops and matching direction of weave [or pattern if fabric is digitally printed].

### Install fabric into locking jaws of track.  Stretch fabric taut; align fabric weave plumb vertically and level horizontally.

## CLEANING

### Section 01700:  Cleaning installed work.

### Trim and remove all loose fabric threads.

### Remove surplus materials and debris.  Vacuum fabric as required.

## EXTRA MATERIALS

### Provide [____] extra panels [of each size].

### Provide extra [____] sq m ([____] sq yd) of fabric.

## PROTECTION OF FINISHED WORK

### Section 01700:  Protecting installed work.

### Protect finished Work from damage or soiling.

END OF SECTION